## Slide 1: SurfingAttack: Interactive Hidden Attack on Voice Assistants Using Ultrasonic Guided Waves
Qiben Yan, Kehai Liu, Qin Zhou, Hanqing Guo, Ning Zhang
NDSS 2020 February 23-26 – San Diego, CA

## Slide 2: Voice Assistants
Read my message
Take a selfie
Calling Sam
Send a message to Sam

## Slide 3: Inaudible Attack
Recent works show that microphone can hear inaudible voice (>25 kHz)
？？？
Yes, how can I help you?
> 25 kHz (Hey Siri)
Input
Amplifier
f
Amp
Low Pass filter
ADC

## Slide 4: Inaudible Attack
Input
Amplifier
f
Amp
Low Pass filter
ADC
Ideally
Actually
+
For Example
f
Amp
If the locates to low frequency range of the filter, then the Mic can hear this Inaudible attack.

## Slide 5: Outline of Inaudible Attack
Backdoor[1]
Dolphin Attack[2]
Lipread [3]
[1] Roy, N., Hassanieh, H., & Roy Choudhury, R. (2017, June). Backdoor: Making microphones hear inaudible sounds. In Proceedings of the 15th Annual International Conference on Mobile Systems, Applications, and Services (pp. 2-14).
[2] Zhang, G., Yan, C., Ji, X., Zhang, T., Zhang, T., & Xu, W. (2017, October). Dolphinattack: Inaudible voice commands. In Proceedings of the 2017 ACM SIGSAC Conference on Computer and Communications Security (pp. 103-117).
[3] Roy, N., Shen, S., Hassanieh, H., & Choudhury, R. R. (2018). Inaudible voice commands: The long-range attack and defense. In 15th {USENIX} Symposium on Networked Systems Design and Implementation ({NSDI} 18) (pp. 547-560).
Inject
Commands
Longer
Range

## Slide 6: SurfingAttack: Features
None Line of Sight: we use solid media to propagate attack signal
Long Range Attack: the longest attack distance can be longer than 30ft
Attack multiple devices simultaneously

## Slide 7: Ultrasonic Guided Waves
Ultrasonic Guided waves is known as Lamb waves
It has two modes based on the wave motion in both sides:
Symmetric modes
Anti-symmetric modes

## Slide 8: Ultrasonic Guided Waves
To understand how waves propagate in solid media:
We should discuss the vibrations on two directions
(x1 and x3) for both modes.
Symmetric modes
Anti-symmetric modes

## Slide 9: Ultrasonic Guided Waves
Symmetric modes
Anti-symmetric modes
Rayleigh-Lamb Equations
Wave frequency
material
Phase-velocity

## Slide 10: Attack Waves Selection
Low dispersion
Low attenuation
Easy excitability
High attack signal reachability
narrowband input signals are most effective in restricting wave dispersal in large and thick plates
lower-order Lamb wave modes(A0)
use a circular piezoelectric disc to generate the signal for its energy efficiency and omni-directivity
Requirements

## Slide 11: Consider a realistic scenario

## Slide 12: Trigger Non-linearity Effect
Design
Baseband signal : 50Hz to 5kHz
Modulated to 25.3kHz
Excite Lamp Wave

## Slide 13: Trigger Non-linearity Effect

## Slide 14: Attack Waves Generation
To preserve the similarity between the recovered voice signal and the original signal, we choose Tukey window for modulation:
Depth of modulation 0.8~1.0
Tukey Window
Baseband Signal
Carrier Frequency
3 Key Factors

## Slide 15: Feasibility
To tackle the 3 factors, we can attack phones as below:
Manufacture | Model | Assistants | Attacks |  | 
 |  |  | Recording | Activation | Recognition
Google | Pixel 1, 2, 3 | Google |  |  | 
Moto | G5 | Google |  |  | 
 | Z4 | Google |  |  | 
Samsung | Galaxy S7 | Google |  |  | 
 | Galaxy S9 | Google |  |  | 
 | Galaxy Note 10+ | Google |  |  | 
Xiaomi | Mi 5, 8 | Google |  |  | 
Huawei | Honor 10 | Google |  |  | 
Apple | iPhone 5, 5s, 6+, X | Siri |  |  | 

## Slide 16: Attack System Design
Voice
Commands
TTS
Module
Speech Synthesis
Voice
Recording
Signal
Processor
Transducer
Tapping Device
Signal Modulation
& Voice Recording
Voice Response
Controller
Attack Device Package
Interactive Voice Commands

## Slide 17: Attacks
SMS Passcode Hacking
Fraud Call

## Slide 18: Stealthiness
You cannot sense the attack:
No sound
No vibration
PZT transducer and waveform generator
are hide under the desk

## Slide 19: Impact of Noise
Google Pixel 1
Attack Distance
30cm
Attack Voltage
9V
Scene | Noises (dB) | “OK google” | “Read my message”
Office | 55-65 | 100% | 100%
Café | 65-75 | 100% | 90%
Restaurant | 75-85 | 100% | 80%

## Slide 20: Impact of Distance
Aluminum coil
No Amplifier
With Amplifier

## Slide 21: Impact of Thickness
Thickness (inch) | Recognition Rate (9V) | Recognition Rate (30V) | Recognition Rate (9V) | Recognition Rate (30V)
1/16 | 100% | 100% | 100% | 100%
1/8 | - | - | 100% | 100%
3/16 | 100% | 100% | 50% | 90%
1/4 | 70% | 100% | 10% | 90%
3/8 | - | - | 0% | 100%
1/2 | 0% | 100% | - | -
1 or 1.5 | 0% | 100% | - | -
Aluminum Metal
Glass
The thicker materials requires higher transmit power

## Slide 22: Impact of Thickness

## Slide 23: Impact of Different Materials
To measure the materials difference, we test
the achievable attack distance on those
materials with 3 phones.
 | Aluminum Metal Sheet (0.3 mm) | Steel Metal Sheet (0.8 mm) | Glass (2.54 mm) | MDF (5 mm)
Xiaomi Mi 5 | 910+ cm | 95+ cm | 85+ cm | 50cm
Google Pixel | 910+ cm | 95+ cm | 85+ cm | 45cm
Samsung Galaxy S7 | 910+ cm | 95+ cm | 85+ cm | 48cm

## Slide 24: Countermeasure
Hardware Layout Enhancement
Enhance microphone to suppress any acoustic high frequency vibration
Interlayer-based Defense
Place device on a soft woven fabric or a multilayers term.
Software-based Defense
  Difference between recovered signal and the baseband signal

## Slide 25: Conclusion
We proposed a voice assistant attack which is:
Low power
Cheap
Inaudible
Long distance interaction
No vibration
Reliable on different tables that have different materials and thickness
Noise resistant
None line of sight

## Slide 26: Thank you!